## Slide 1
Auto EA-SORAN: AI-Native Energy Optimisation for 5G RAN
How it works: A Simu5G digital twin feeds a Python multi-agent loop (Prediction → Optimisation → Feedback → Orchestration) over ZeroMQ/CSV files to reduce base-station energy while keeping QoS within policy.
Team NoWiresAttached

## Slide 2
The Challenge: RAN Power Consumption
1
Dominant energy bills:
5G's capacity boost inflates RAN power use, dominating operator energy expenses.
2
Idle waste:
Even with minimal traffic, many base station (BS) components remain active, wasting energy.
3
Inflexible rules:
Static settings fail to adapt to dynamic traffic and varying service level agreements (SLAs) like eMBB, URLLC, and mMTC.
The Goal: Develop a safe, automated system to adjust BS settings based on real-time demand—without compromising Quality of Service (QoS).

## Slide 3
Why Is Energy Optimisation Difficult?
Complex Dependencies: Base station energy use hinges on configuration (TX power, carriers, bandwidth), traffic (PRB utilisation), and energy-saving (ES) modes (micro/deep sleep).
QoS Risks: Blindly adjusting settings can negatively impact throughput and latency.
We require a closed-loop system that predicts, optimises under policies, and verifies safety before implementing any changes.

## Slide 4
Our Solution: AI-Powered Optimization Loop
Digital Twin:
Leverage Simu5G to monitor KPIs and simulate actions on gNodeBs.
Four Python Agents (ZeroMQ):
Prediction: Utilises a Keras ANN for short-term energy forecasting.
Optimization: Proposes energy-saving strategies.
Feedback: Ensures proposed plans align with established policies and thresholds.
Orchestration: Implements approved modifications within the Simu5G environment.
Goal: Reduce energy consumption while maintaining QoS within defined parameters.

## Slide 5
Integration within the 5G Service Landscape
Our optimisation techniques adapt based on the specific service type, ensuring tailored energy savings.
eMBB (Enhanced Mobile Broadband)
Prioritise throughput efficiency.
Employ micro-sleep and subtle TX-power adjustments.
Maintain at least p95 DL rate.
URLLC (Ultra-Reliable Low Latency Communications)
Focus on minimal latency and loss.
Employ conservative strategies.
Implement immediate rollback for violations.
mMTC (Massive Machine Type Communications)
Cater to sparse traffic scenarios.
Utilise deeper sleep states and carrier off windows.
Employ broader operational thresholds.
Policy-driven optimisation: Policies adapt savings to service needs.

## Slide 6
Deployment Pathways for Real-World Networks
O-RAN Integration
Deploy Prediction/Optimisation/Feedback as near-RT RIC xApps. Orchestrate actions via E2 interface to gNBs; monitor KPIs via SMO/OAM framework.
Simu5G Validation
Utilise Simu5G for high-fidelity testing. Train and validate policies and actions safely before real-world pilots.
Benefit: Provides a safe, controlled environment for testing and refining energy optimisation strategies.

## Slide 7
Core Operational Dynamics
Key Elements
gNodeB (BS), PRB utilisation, TX power, carriers, bandwidth, ES modes (micro/deep sleep) are optimised.
Dynamic Loop
Real-time BS metrics → Prediction (estimate energy use) → Optimisation (select action) → Feedback (policy enforcement/rollback) → Orchestration (apply changes).
ZeroMQ Advantage
Enables low-latency, straightforward Python↔C++ communications.

## Slide 8
System Architecture Overview

## Slide 10
Detailed Sequence of Operations

## Slide 11
Deciphering Energy Conservation Metrics
Power (W): Measures instantaneous energy consumption.
Energy (J or Wh/kWh): Represents power use over time.
Simu5G Integration: Provides power states (active, micro, deep) and a power formula related to PRB utilisation:
We integrate power over a given period to determine energy consumption and benchmark against baseline results.
Result Presentation:
% Energy Saved = (Ebaseline - Eoptimised)/Ebseline x 100%
Absolute kWh saved for the specified duration.

## Slide 15
OUTPUT & CONCLUSION

## Slide 16
Output screenshots

## Slide 17
THE SHAP GRAPHS

## Slide 18
THANK YOU!